SIA "GRAVITIS ENTERPRISE LIMITED"
Lauku iela 7 - 4, Cēsis, LV-4101, Latvia
Technical Drawing Package

Solar Eclipse Plastic Glasses (EGP-FIT-TDP)
Document Title:	Technical Drawing Package
Product	Solar eclipse glassses. Model: EGP-FIT-TDP
Document No.:	EGP-FIT-TDP-001
Revision:	A
Date:	5/2/2026
Status:	FOR NOTIFIED BODY SUBMISSION

	Name	Signature	Date
Drawn By:	Māris Grāvītis		# TODO
Checked By:	Māris Grāvītis		# TODO
Approved By:	Māris Grāvītis		# TODO

# Revision History

Revision	Description Of Changes	Date	Approved By
A	Initial Release	05/02/2026	Māris Grāvītis

# Fabrication Specification (EGP-FIT-FAB-001)
## SPECIFICATION DATA
Parameter	Specification
Product Model	EGP-FIT (Oversized Fit-Over)
Standard	EN ISO 12312-2:2015 (PPE Category II)
Frame Material	Injection Molded Polypropylene (PP)
Filter Material	Silver-Black Polymer (0.12mm nominal)
Optical Density	OD ≥ 5.0 (Transmittance ≤ 0.0032%)
Protection	100% UV / 100% IR Block

## MANUFACTURING & QUALITY NOTES
1. LIGHT LEAKAGE (CRITICAL): 100% inspection required. There must be zero light leakage around the perimeter where the filter meets the frame.
2. LENS RETENTION: Filter lenses must be securely retained. Any loose lenses are a critical failure.
3. SURFACE QUALITY: Filter surface must be free from pinholes, scratches, or delamination.
4. MARKING: Due to the specific nature of the surface/production, no markings are applied directly to the product. All mandatory regulatory markings (CE, Notified Body No, Manufacturer, Standard) are applied to the Primary Packaging. (See Packaging Artwork: PKG-PLASTIC-SERIES-1PK-OUTER-001).